## Slide 1
Chapter 14 – IFPO - CPO
Fire Prevention, Detection and Response

## Slide 2: Purpose
Fire is one of the most hazardous threats to life and property.
Understanding how combustion occurs, how to detect fire, extinguishment methods and effective strategies for protection of life is essential for security professionals.
Key Terms
Fire Triangle
Extinguisher Types
Stand Pipes
Containment
Arson
Fire Basics
The Fire Triangle
For fire to occur, three elements must be in place:
Fuel, (the material that will burn,) oxygen and heat
Without the presence of ALL THREE components, a fire cannot begin or be sustained.

## Slide 3: Inspection of Hazardous Areas
Areas that are cluttered have an increased chance of fire. They should be frequently inspected until properly cleaned:
  Boilers, heaters, furnaces
  Laundry areas
  Electrical equipment and breaker rooms
  Storage areas for flammable liquids
  Vehicle storage areas
  Work areas with combustible liquids (oils, paints, etc.)
  Smoking areas
  Cooking areas

## Slide 4: Detection Methods
The two methods of fire detection are:
Human Observation
Human observation is often more effective, since it allows for the use of reasoning and judgment to determine the nature of actual situation.
Electronic Systems
Electronic systems are highly effective:
Use of sensors for multiple areas:
  Smoke
  Rapid increase in temperature
  Early combustion of airborne particles
The ideal detection program is a combination of human observance and electronic monitoring.

## Slide 5: Fire Types
The basic classes of fires are as follow:
Class A: Common materials - paper, wood and cloth.
Class B: Flammable liquids - Petrol, kerosene, compressed gas like propane, etc.
Class C: Electrical fires
Class D: Combustible metals – Require special equipment to handle
Class K: Oils and greases normally found in commercial kitchens

## Slide 6: Extinguishers and Their Uses
Common extinguisher types and class(es) of fires they are designed to be used on:
Dry Chemical: Expels a pressurized, nonflammable stream of powder. Used on:
  Class A, B and C fires
Carbon Dioxide: Produce a cloud of snow-like particles. Used on:
  Class B and C fires
Water-Base: Used on Class A fires ONLY.
Halogenated Units: Uses a chemical that leaves no residue. Cool and smother fire. Used on:
  Class A, B and C fires
Foaming Agents: Produce a foam layer that blocks the flow of oxygen. Used on:
  Class A and B fires

## Slide 7: Permanent Extinguishing Hardware
These are elaborate extinguishing devices that are installed in/on buildings.
Automatic Sprinklers: Operate through a spring-loaded valve that opens when exposed to a certain minimum temperature.
Range-Hood Systems: Used in kitchen areas to grease and other common kitchen fires. Triggered manually by people who observe a fire.
Stand Pipes: Are like an extension of the fire hydrant. Provides the fire fighters with a source of water to extinguish the fire.

## Slide 8: Containment
Starts with design limitations and construction requirements:
Fire-resistant doors, designed to resist the spread of a fire for certain periods of time, aid greatly in the containment of a fire.
Must be installed in accordance with manufactures requirements.
Security should patrol to confirm that fire doors are in proper condition and closed.
Fire Plans
As part of the formal plan, alarm systems should be regularly inspected and tested to ensure proper functioning.
Once developed and approved, people must be trained and the plan MUST be exercised. An untested plan is simply a concept.

## Slide 9: Fire Plans
The most effective step in any fire prevention, detection and response program is the development of a fire plan.
Developing the plan must be done in cooperation with those expected to execute the plan.
Senior management must support and approve.
Fire marshal might have to review and approve the plan (check local regulations.)
Plan should be shared with area first responders.
The written plan should include the following:
  Emergency contact names and numbers
  A detailed chain of command
  Explanation of equipment available and inspection/maintenance schedule
  Explanation of training and frequency of retraining
  Charts and diagrams of the property
  Detailed explanation of responsibilities for:
    Prevention aspects
    Response aspects

## Slide 10: Arson
An intentionally set fire, usually for one of these reasons:
  Monetary/Insurance fraud
  Psychological disorders
  To hide prior criminal activity
Best protective measures are:
  Highly visible patrols
  Securement of rooms with flammable materials
Fire as a Weapon
Officer awareness of patterns or materials being delivered are important for overall situational awareness.
The security officer’s observations and actions are the front-line of preventing the use of fire as a weapon.
All security personnel should be trained in plans involving evacuation and shelter-in-place.