## Slide 1
Chapter 16/16A – IFPO - CPO
Contraband Detection Technology
Unmanned Aerial Vehicle Usage 21st Century

## Slide 2: Detection Equipment
Can be used for both access and egress
The selection of equipment should be based on:
  Types of inspections being conducted
  The protection level required
  The sophistication and type of threat
Selection will be defined by organizational policies and procedures.
Selection also based on:
  Durability and reliability of equipment
  Area of detection
  Volume of traffic or articles to be screened
  Aesthetic effect on and cultural fit with environment
  Life cycle-cost of the equipment:
    Initial cost, Installation, Operation, Maintenance costs, any other fees and/or taxes

## Slide 3: Metal Detection
It is essential that the protection officer conducting the manual inspection displays the utmost level of professionalism and courtesy.
If possible, the gender of the officer should be the same as the person being screened.
Metal Detection Devices
Walk through or Non-portable
  Airport, schools, high security facilities and courthouses
Hand held devices may be necessary to use when an automated system is activated or triggered at
Used by police for locating:
  Weapons, Bullets, Knifes, etc. for investigative purposes

## Slide 4: Metal Detection Technology
Magnetometers
  Attracted by ferromagnetic materials or metals attracted by a magnet.
  Cannot detect metals like copper, aluminum, zinc.
Pulse Field Detectors
  Complex frequency waves
  Produce an Eddy current
  If metal detected, sounds an alarm
Continuous Wave Devices
X-Ray Detection
Devices that are capable of detecting drugs, metallic items, explosives and some food items.
Concerns when using:
  Operator fatigue from extended periods of monitoring.
  Improper assessment interpretation
Mistakes reduced through proper training.

## Slide 5: Explosive Detection
Used for preventing the introduction of hazardous materials into the area.
Must be able to identify the five basic components of an explosive device:
    Power source such as a battery
    Explosive material
    Detonator or blasting cap
    Triggering device such as a watch or clock
    Connecting wires
Chemiluminescence Detectors
  Can detect explosives such as RDX and PETN through photochemical means from vapor samples collected.
Backscatter Technology
  Detects organic compounds and narcotics using X-ray reflection.
Computed Tomography
  Uses a computer program to scan packages for explosives.
  Uses X-ray scanners that provide a 3-D image

## Slide 6: Canine Detection
Offer great portability in a variety of applications.
Olfactory senses are 10,000 to 10,000,000 times more powerful than a human’s.
Used in detection of:
  Explosives
  Humans (live or dead)
  Drugs
  Chemical weapons
  Organic materials (food, plants, etc.)
Used to enhance security patrols.
Dual trained as detection and bite dogs.
Enhances the defense and protection of the handler.
Not susceptible to false alarms.
Add a deterrent value.
Well-trained dog and handler can work 8-10 hours.

## Slide 7: Electronic Article Surveillance
Uses magnetic, VHF/microwave, or barcode sensors to detect fraudulent activity.
Used in:
  Libraries
  Retail stores attached to cloths or item
  Can be used for assisted living to track people
Alarm sounds when activated
Radio Frequency Identification(RFID)
  Can detect fraudulent activities from the raw material stage to manufacturing to retail to end user
  Offers real-time data
Value Deprivation Tags
  Attached to item
  Does not activate alarm
  Cannot be removed without damaging the item
  Similar item explodes on clothing if removal is attempted without proper tool.

## Slide 8: Unmanned Aerial Vehicles
Remotely controlled or guided through software-controlled flight plans working with GPS.
New rules and laws governing unmanned aerial systems (UAS) changed in 2019.
Changes found in FAA Guidelines for Unmanned Aircraft Systems (UAS)
To fly unmanned aircraft over 55lbs, operators need to apply for an exemption.

## Slide 9: Security Application for Drones
Possible uses for drones include:
  Civil security – operations against looters or interlopers
  Anti-piracy
  Surveillance and apprehension
  Crime scene photography
  Monitor traffic flow
  Monitor serious vehicle, train, boat, aircraft collisions
  Patrol operations
  Anti-trespasser patrols

## Slide 10: Drones: Accident Reporting
Pilot in command must report an accident to the FAA within 10 days if:
  Resulted in death, serious injuries or loss of consciousness.
  Damage to any property other than the UAS.

## Slide 11: Gunshot Detection
Used for both indoor and out detection of gunshots.
Indoor Detection:
  Uses dual sensors to detect gunfire and relay information via floor map plan with shot locations.
  Texts, email and other notifications to key personnel and building occupants.
  Can be integrated with surveillance cameras.
  Can initiate lock-down procedures.
  Provide immediate notification to first responders.
Outdoor Detection:
  Uses acoustic and computer-based signal processing to pinpoint small arms fire.
  Immediately reports precise location of shooter to authorities.
  Can be mounted on vehicles or fixed structures.
  Can be carried by patrolling personnel.

## Slide 12: Alarm Response
A systematic process for investigation, isolation and handling of the person, item or area must be developed.
Have a process in place
Policy and procedures
Rational and calm
Report to supervisor
Reduce threat and protect life
Do not attempt to move item
Hands on inspection only as last resort
Force should only be used under severe circumstance (use of force continuum)
Summary
No single detection technology is suited for all applications.
Must determine a threat basis
Must be matched to the organizational objectives
Human interaction and assessment drives the effectiveness
Cost and training is a critical component