## Slide 1
Chapter 31 –IFPO- CPO
An All-Hazards Approach to Hazardous Materials

## Slide 2: Purpose
A security professionals ability to recognize an incident involving hazardous materials(Hazmat) is critical. Security must know how to identify the presence of Hazmat and know what their role is within the response plan.

## Slide 3: Hazardous Material
A hazardous material is anything that has the potential to cause harm to people or the environment (plants, animals, and waterways) if released in an uncontrolled manner.
Classification system includes 23 classes and divisions
Liquids of any sort, including water, when released at the wrong time or the wrong place, can create a life-threatening or facility-threatening situation.

## Slide 4: Seven Immediate Threats
Explosives
Mass explosion hazards
Projection hazards
Fire or incendiary hazard
Dangerous when wet materials
Toxic inhalation hazards
High level radioactive materials

## Slide 5: Role of the Protection Officer
Education and training is the first line of defense.
The protection officer must be familiar with all hazardous materials found within his/her area of operations.
Weather-related incidents and hazardous materials incidents represent the majority of recurring serious incidents in the workplace.
The protection officer should be aware of evolving technologies such as:
  Ethanol-enhanced fuels
  Lithium ion batteries
  Compact fluorescent lights (CFLs)
  Pressurized fire extinguishers
  Aerosol lubricants and deicing materials

## Slide 6: Role of the Protection Officer
Examples:
Compact fluorescent lights (CFL’s):
  CFL’s contain mercury.
  Illegal to dispose in trash bins.
  A single broken CFL bulb is not cause for alarm. However is officially an “event” because mercury is released
Fire Extinguishers:
  Fire extinguishers are classified a hazardous material because the heat generated from a fire can cause them to explode.

## Slide 7: Hazardous Materials Incidents
A protection officer’s primary objective must always be to survive so that they can continue to provide that protection to the general public.
The protection officer must understand how to evaluate and take the action that will bring the correct resources to bear for the many different types of incidents that can occur.
Rule number one with hazardous materials incidents is to always approach from upwind, uphill, or upstream.
Know how to evaluate and take actions.
  Self protection
  Approach from upwind, uphill, or upstream
  Know where to find information on the product
  Evacuation
  How to contain
For protection officers, the first step is self-protection, the second is material identification, the third is to evacuate as necessary and activate the appropriate contingency or response plans, and the last step in most circumstances is to provide containment.
Even for the smallest of spills involving the most benign chemicals, no action should be taken until the material has been positively identified and appropriate actions confirmed.

## Slide 8: Tools and Resources
Small releases of less deadly materials can be handled by anyone with the right formal training, basic knowledge of hazardous materials response, an understanding of the risks and protocols, and access to the material safety data sheets (MSDS) to properly identify risks associated with each specific incident or material.
The most universally accepted method to identify and classify hazardous materials comes from the world of transportation.
DOT guideline 49 CFR parts 100 to 180 “Hazardous Materials Regulations”(HMR)
Most comprehensive book on hazards
  Emergency Response Guide 2016 ERG
  National Incident Management System (NIMS)
  Incident Command Systems (ICS)
  NFPA-Diamond Designation
  4 colors
  Blue, yellow, red and white
  What materials are contained within the structure

## Slide 9: Tools and Resources
One of the first things a professional should do in a new job, or for that matter in a new location, is to identify all the hazardous materials that enter, are used in, or leave, the facility.
A security professional should review all the MSDS information for each worksite under their protection and know exactly where to find that information in case an incident occurs.
There are going to be times when the most appropriate action is to turn and run!
Material Safety Data Sheets (MSDS) properly identify risk associated with each specific incident or material.

## Slide 10: Initial Response
The basic steps to follow
  Identify the substance released
  Determine the quantity released
  Activate appropriate contingency plan
  Determine extent of damage
  Perform site security
Always stay uphill until the substance is identified.

## Slide 11: Identify the Substance Released
Always stay upwind, uphill, and/or upstream of any hazardous materials release until able to identify it.
One way to identify material at the workplace is to ask the person who was using it.
MSDS, ERG, labels, etc.
Labels are the least accurate
Identifying the four-digit number unique to a spilled material is always the best and most accurate way to determine appropriate response actions.

## Slide 12: Diamond Designation
Diamond Designation is in four colors and conveys to responders the nature and severity of materials contained in buildings.
Determine the Quantity
After identifying the substance, it is important to determine how much of it has been released.
Never go near the area unless properly trained in the required level of PPE; this prevents the professional from inadvertently becoming another victim of the incident.
Activate the Appropriate Contingency Plan
The protection professional should be familiar with the organization’s HAZMAT response plan.
If no plan in place, notify the public agency involved in handling HAZMAT incidents for the area. Usually this will be the local fire department. When they arrive on the scene, they will take command and control of the situation.

## Slide 13: Determine the Extent of Damage
After the material and amount released have been determined, it is necessary to evaluate the extent of any damage that may have been caused.
It is extremely important to keep clear of the area and to keep others clear until this determination has been made.
Any injured people should be treated by qualified first aid or medical personnel as soon as they are safely removed from the contaminated area.
Perform Site Security
Site security simply means keeping onlookers and bystanders out of the contaminated area.
Media:
  They take risks just to get a story
  They sneak past security or cross barricades putting themselves and others at harm.
  They interfere with the operation
  Fail to follow safety precautions
  They risk becoming exposed/victims
  They increase the workload