## Slide 1
Chapter 37 – IFPO -CPO
Physical Security Concepts and Applications

## Slide 2: Purpose
Physical security is a vital part of all security planning and is fundamental to the protection of people, property and assets. Without physical security protection would be difficult or even impossible.
What is Physical Security Planning?
It is a recognized security process that, if followed, will result in the selection of physical countermeasures based on appropriateness. Countermeasures should also be justifiable from a cost point of view.
The organization identifies its:
  Assets
  Risks
  Threats
Which then determine the level of appropriate countermeasures that are required based on this process.

## Slide 3: Risks
Risks are usually categorized into three categories:
  People: Human resources are usually the most critical asset within any organization, and as such, must receive a stronger consideration when assessing risk.
  Property: Physical property or intellectual assets.
  Legal liability: Legal risks can also affect people and property but need to be considered as a separate category. This is due, in part, to the extent that lawsuits affect the security industry these days.

## Slide 4: Security Planning Steps
The security planning process consists of the following five steps:
Assets identified
Loss events exposed
Occurrence probability factors assigned
Impact of occurrence assessed
Countermeasures selected

## Slide 5: Security Planning Steps
Assets identified:
  People are the most valuable asset.
Loss events exposed: Threats can be grouped into the following categories:
  Industrial disasters
  Natural disasters
  Civil disturbances
  Crime
  Other risks: A catch-all for threats that do not fit into the other categories: Cyber-crime, loss of utilities, etc.
Occurrence probability factors assigned:
  Quantify the possibility that the threat will occur.
  This is probably the most difficult step in the process.
  The following affect probability:
    The physical composition of structures
    The climatic history of the area
    The nature of activity on the property to be protected
    Criminal history of the area
    Past incidents at similar organizations & Community Conflict in the area

## Slide 6: Security Planning Steps
Impact of the occurrence assessed:
  Impact for almost all organizations has a bottom line of dollars and cents.
  The most important thing to remember is that dollar losses may be either direct or indirect.
  Direct costs are those that can be directly assigned as the value of the asset that has been lost or damaged.
  Indirect losses are those costs associated with the loss that would not have been incurred if the loss event had not occurred. An example is downtime.
Countermeasures selected:
  This is the final step in the planning process.
  The initial step is to decide on the level of protection needed; the level can range from low to very high.
  Use a definable, justifiable, and systematic approach.
  By standardizing the process, mistakes are less likely to occur and more accurate calculations can be made.
  Think in terms of security-in-depth.

## Slide 7: Security-In-Depth
Security-in-depth, also known as layered protection, is a concept that means placing a series of progressively more difficult obstacles in the path of an aggressor, requiring the aggressor to have more skills and more complex equipment and tools. These obstacles are often referred to as lines of defense.
  The first line of defense is at the property line.
  The second line of defense is the exterior of buildings.
  The third line of defense is interior controls or object protection.
Integrated Protection
Integrated technologies offer expanded capabilities.
Effective planning will result in a cost-justified, integrated protection program.
An integrated protection program results from a systems approach to selecting controls.
The following are two important points in relation to using a systems approach:
  The whole, a swell as each separate part, must be considered.
  Design should allow for an acceptable level of redundancy, without any unnecessary duplication of effort.

## Slide 8: Security Lighting
Security lighting has three primary objectives:
It must act as a deterrent to intruders.
It must make detection likely if an intrusion is attempted.
It should not unnecessarily expose patrolling personnel.
Lighting systems are often referred to as “continuous,” “standby,” and “movable” or “emergency.”

## Slide 9: Lighting Systems
Continuous: Most commonly used. Lamps are mounted on fixed luminaries and are normally lit during the hours of darkness.
Standby: Different from continuous lighting in that the lamps are only lit as required.
Movable or emergency: Portable lighting that may be used to supplement either continuous or standby lighting.
Light sources may be incandescent, gaseous discharge, or quartz lamps. The common lightbulb emits incandescent light.

## Slide 10: Types of Lighting
Gaseous discharge: Mercury vapor (bluish) Sodium vapor (yellowish.) Color identification is difficult and unreliable. Ex: street lighting.
Light Emitting Diode (LED): Typically small, and integrated optical components.
Metal halide: Very effective when used with color network video cameras. Very expensive to use. Ex: Sports arena type lighting.
Incandescent: Very inefficient for security purposes. Ex: Home lighting.
Quartz: Bright white light. Ex: Spotlights, Floodlights

## Slide 11: Lighting Application Considerations
When designing a protective lighting system, consider three lines of defense: the perimeter, open yards, and building exteriors.
Illumination of transaction areas, such as ATMs, fare handling machines, and other online transaction stations should be adequately illuminated, independently of the surroundings.
All accessible exterior lamp enclosures should be in tamper- or vandal-resistive housing.
If protective lighting is to be in an area that may be subject to explosions, the housings should be explosive-resistant.
Consider the impact that additional lighting will have on the neighbors.

## Slide 12: Security Glazing
Five types:
Safety/fire
Burglar/vandal-resistive
Bullet resistive
Explosion resistive
Special purpose

## Slide 13: Safety/Fire Glazing
Tempered:
  Safety glass several times stronger
  When it does break, it disintegrates.
Wired:
  Wire embedded in the glass provides extra strength.
  Listed by Underwriters Laboratories as fire-retardant.
Safety/fire-retardant glass used in passageways, entrance doors, sliding doors, bathtub enclosures, shower doors.
Burglar/Vandal Resistive:
  Laminated glass, wired glass and acrylic, and polycarbonate plastics.
  All much strong than safety/fire retardant glass.
Bullet Resistive:
  Consists of multiple piles of glass and plastic material laminated together.

## Slide 14: Security Glazing
Explosion Resistive:
  Designed by an engineer using specific standards which include two American Society for Testing and Materials (ASTM) standards: ASTM F1642 (air-blast loadings), ASTM F1233 (ballistics and physical attack); as well as the UL standards for burglar-resistant and bullet-resistant glazing.
Special Purpose:
  Transparent mirror glass, coated glass, heated glass, and rough or patterned glass.
  Used for privacy with natural lighting and surveillance.

## Slide 15: Intrusion Detection
Every intrusion detection system is meant to detect the following:
  Unauthorized entry
  Unauthorized movement within
  Unauthorized access to controlled areas or objects
There are four components to an intrusion detection system:
  Detectors/sensors
  System controls
  Signal transmission
  System monitoring

## Slide 16: Detectors and Sensors
Typically integrated with physical barriers, such as a door or window, and must take environmental conditions into consideration to be effective.
Different types of detectors and sensors include:
  Magnetic switches: Door or window contacts
  Metallic foil: Narrow strip of metal designed to break.
  Vibration: Shock sensors
  Ultrasonic: Motion detectors in a enclosed area
  Photoelectric: A beam of light reflected
  Infrared: Area detector: measure radiated energy and ambient temperature
  Microwave: High frequency radio waves to establish a protected area.
  Dual technology: Combines two technologies into a single sensor.
  Video motion: Network video cameras, which incorporate video content analysis to identify predetermined behaviors such as a bag left behind, facial recognition, license plate recognition, and virtual fence crossings.

## Slide 17: System Controls
System controls consist of components that transform individual detectors/sensors into a network of intelligence-gathering devices.
System controls include data processing equipment, signal transmission equipment, on/off and reset controls, backup power supply, LED system status indicators, and any other equipment specific to a particular system.
Signal Transmission
The signal transmission equipment is the means by which an alarm is raised. This equipment may simply activate a local siren, send a message to a smart device, or it may send a signal over a wire to a remote monitoring location.

## Slide 18: System Monitoring
There are three options:
  Local
  Proprietary
  Commercial
Local: Can integrate with a computer, smartphone, or iPad to communicate an alarm. Used in many private residences.
Proprietary: System is monitored on-site or remotely by employees of the owner of the protected premises.
Commercial: Falls into two categories: monitoring stations or answering services. They are either Underwriters Laboratories (UL) approved, or they are not. UL-approved is the best guarantee of quality service.

## Slide 19: Card Access
The decision to use or not to use a card access system should be based on the perceived need for accountability and the accompanying financial considerations.
An objective statement for a card access system might read: “To economically eliminate the inherent security weaknesses in key access systems by electronically supervising and documenting the activities or persons authorized to access the property.”

## Slide 20: Card Access
To be useful, a card access system should have the following minimum capabilities:
  Restrict access by authorized persons to certain locations, times, and/or days of the week.
  Allow controlled after-hours access to selected areas within.
  Control after-hours access to a parking area.
  Selectively control after-hours use of elevators.
  Maintain a record of all valid and invalid use of cards.
  Provide an audit trail permitting a digital record of persons on the property at any one time.

## Slide 21: Card Access
There are numerous types of cards:
  Magnetic coded: Magnetic spots on card
  Magnetic strip coded: Like a commercial credit card
  Proximity coded: Must be held near a reader to gain access
  Weigand coded: Contains a series of parallel wires
  Hollerith: Small rectangular holes punched in it
  Optical coded: Uses a bar code
  Smart-card chip or Integrated circuit card: Pocket sized with embedded circuits.

## Slide 22: Card Access
The information contained in the normal employer ID card can be incorporated into any access card:
  Company name and logo
  Details of cardholder
  Name
  Department
  Date of birth
  Signature
  Photograph
  Conditions of use (restrictions)

## Slide 23: Smart Access Control
In addition to card access, another form of access control is where mobile or Smartphone users just hold their phone to a Bluetooth or Near Field Communications (NFC) reader, and the door will unlock, and the permissions (log-in credentials) are checked in the background.

## Slide 24: Locking Hardware
Locking hardware can be categorized as mechanical, electrical, or electromagnetic, and as either security or non-security.
Quality mechanical security locks should be used for all of the following:
  Perimeter openings
  Doors that control/restrict internal movement
  Doors to sensitive/restricted area
Only deadbolt locks should be considered. Theboltshouldofferaminimumofa1-inthrow, where the bolt passes 1-in into the door frame.
Electric locks are particularly suitable for the following:
  • Remote control of the after-hours pedestrian entrance door
  Grade-level emergency exit doors
  Exit doors from stairwells to grade level
  All stairwell doors
Electromagnetic locks are particularly suitable for use on emergency exit doors, as there are no moving parts that can accidentally become jammed.

## Slide 25: Network Video
Network video has three major roles in any physical security program:
  To deter crime or unwanted activities
  To allow the ability to witness an act as it occurs
  As an investigative tool after an act has already been committed
There are three main views that a standard network video system should provide, depending on the application requirements:
    Identification of any subjects.
    Identify the actions within a scene.
    Identify the scene where the act occurred.
Subject identification:
  Based on the principle that whoever or whatever is viewed must be identifiable beyond any reasonable doubt.
Action identification:
  Is a view that can assess what has occurred within a given area.
Identification of a scene view:
  Based on being able to identify where an act took place.

## Slide 26: Network Video Components
Cameras: The two most common are:
  CCD –Charged coupled device
  CMCS –Complementary metal oxide semiconductor
Lenses
  Fixed: Offers only a single point of view.
  Varifocal: Offers a range of views as long as range is within lens capabilities.
  Zoom: best for situations in which the lens needs to be refocused, should one change the field of view.
Housings
Monitors
Sequential Switches
  Allows for reviewing multiple cameras on one monitor.
Motion Detectors
  If movement occurs within the field of view of the camera lens, an alarm will sound at the control center.
Pan/Tilt/Zoom
  The need to use several cameras to cover an area or activity can be avoided by carefully positioning one camera and providing pan/tilt/zoom features.

## Slide 27: Network Video Components
Controls
  in addition to the normal television controls, controls will be required for whatever special features are built into the system.
Consoles
  Care must be exercised to ensure proper ergonomics.
Video Recorders
Date/Time Generators
  Where no immediate incident response capability is available, or if the recording may be required as evidence in court.

## Slide 28: Safes and Vaults
Safes and vaults are designed to offer varying levels of protection from specific risks— namely burglary, robbery, and fire.
Locks
  Safes are available with three types of locking systems:
    Single combination
    Single key lock combination
    Dual combination

## Slide 29: Safes and Vaults
Burglary-Resistive Safes
In addition to their actual construction, burglary-resistive safes have several protective features:
  Locks
  Interior design
  Depository
  Time locks / Time delay locks
  Relocking device
  Extra weight
  Floor anchoring
  Counterspy dials

## Slide 30: Safes and Vaults
Burglary-Resistive Vaults
Any storage container specifically designed to resist forcible entry and large enough to permit a person to enter and move around within while remaining upright, can be considered a vault.
Vault construction consists of: reinforced concrete walls, floor and ceiling, and a specially constructed vault door.
Fire-Resistive Containers
  Insulated safes, filing cabinets, and record containers that offer varying degrees of protection to contents from exposure to heat are available.
  Two very important points in relation to fire resistive containers are:
    Paper records will be destroyed at temperatures in excess of 350°F (159°C).
    Computer tapes/disks will be destroyed at temperatures in excess of 150°F (66°C).

## Slide 31: Fencing
Fencing has been used throughout history as a defense against enemies—the walled city of Pompeii dates to 800 BC, and it was not uncommon for the complete frontiers of kingdoms in China to be walled (origin of the Great Wall of China). Closer to home, the old city of Quebec remains the only enclosed city in Canada and the United States.

## Slide 32: Fencing Rules
Minimum of 7 feet in height excluding top overhang.
9-gauge or heavier.
Mesh openings must not be larger than 2” square inches.
Fabric must be fastened securely to rigid metal or reinforced concrete posts set in concrete.
No more than 2 inches between the bottom of the fence and the ground.
Fabric extend below the surface of soft/sandy ground.
Top overhang should face outward and upward at a 45-degree angle.
Overhang supporting arms should be firmly affixed to the top of the fence posts.
Overhang should increase the overall height of the fence by 1 foot.
Three strands of barbed wire, spaced 6 inches apart, should be installed on the supporting arms.
A clear zone of 20 feet or more should exist between the perimeter and exterior structures.
Where possible, a clear zone of 50 feet or more should exist between the perimeter barrier and structures within the protected area.

## Slide 33: Fencing
Vehicular and pedestrian gates in the perimeter fence should be kept to a minimum.
All openings in the perimeter fence should be equipped with gates.
Typically, security control is provided at the first defensible point.
Beyond these points, a secondary secure perimeter should be established.
Fencing is a barrier that will only delay the determined would-be intruder.

## Slide 34: Underwriters Laboratories (UL)
Is a recognized certification organization for security equipment, security systems, and security monitoring,
UL has created safety standards for every device, system, and monitoring center that they certify.
UL criteria are important in physical security, as they help to reduce potential litigation by conforming to specific standards.
Integrated Security Systems
Highly functional integrated systems allow for real-time monitoring of systems via a security operations center and a smart device (portable telephone or iPad).
Integrated systems allow for multiple functions to be accomplished in a near simultaneous fashion.

## Slide 35: Education
Career planning
Employers are searching for dedicated security officers
Work exposure is critical
Professional designations through
  ASIS
  IFPO
Physical Security Professional
The ASIS Board Certified Physical Security Professional (PSP) designation focuses on one’s proficiency in three major domains of knowledge:
  Physical security assessment
  Application, design, and integration of physical security systems
  Implementation of physical security measures
ASIS International does have eligibility requirements, which include work experience, to sit for the PSP certification exam.